KD CORE ADJUSTMENT

# PHASE TO PHASE UNIT

- Disconnect current leads.

- Back off stationary contact and adjust spring tension until moving contact just floats.

- Jumper C2C  (rear lead) to the side of R2C  that has multiple leads on it.  (Look at Internal Schematic for the KD you’re testing,  you may be able to jumper across some component such as RC  in the .75-21.0 KD-10, or CC in the 1.3-36.0 KD-10 more easily).

- Apply 120 volts to terminals 7 and 8.

- Adjust core until contacts just float.

- Remove jumper between C2C and R2C (or component).

- Jumper terminals 7 to 9 and apply 120 volts to terminals       7 and 8.

- Adjust:

  - KD-4/41,  RAC until contacts just floats.

  - KD10/11,  reactor  XLAC  until contacts just float.

- Readjust spring tension and contact gap.

THREE PHASE UNIT

- Be sure the current leads are disconnected.

- Back off stationary contact and adjust spring tension until moving contact just floats.

- Jumper terminal 8 to C3C  (front lead).

- Apply 120 Vac to terminals 7 and 8.

- Adjust core until contacts just float.

- Remove jumper between terminal 8 and C3C.

- Jumper terminal 7 to 9 and apply 120 volts to 7 and 8.

- Adjust:

  - KD-4/41,  R3A until contacts just float.

  - KD-10/11, R3F  (coarse) and P3A  (fine) until contacts just float.

9.  Readjust spring tension and contact gap.

## KD,  BOTH CORES ADJUSTMENT

- Be sure the current leads are disconnected.

- Back off stationary contact and adjust spring tension until moving contact just floats.

- (Phase to Phase unit) Jumper C2C (rear lead) to the side of R2C with multiple leads on it.      (Look at Internal Schematic for the KD you’re testing, you may be able to jumper across some component such as RC in the .75-21.0 KD-10, or CC in the 1.3-36.0 KD-10 more easily).

- (3 Phase unit) Jumper Terminal 8 to C3C (front lead).

- Apply 120 Vac to terminals 7 and 8

- Adjust cores until contacts just float.

- Remove jumpers.

- Jumper terminal 7 to 9 and apply 120 volts to 7 and 8.

- Adjust    (Phase to Phase Unit):

a.  KD-4/41,   RAC until contacts just float.

b.  KD-10/11, reactor XLAC until contacts just float.

10. Adjust    (Three Phase Unit):

a.  KD-4/41,   R3A until contacts just float.

b.  KD-10/11, R3F (coarse) and P3A (fine) until contacts just float.

11. Readjust spring tension and contact gaps.